## Slide 1: IX: A Protected Dataplane Operating System for High Throughput and Low Latency
Adam Belay, George Prekas,
Samuel Grossman, Ana Klimovic,
Christos Kozyrakis, Edouard Bugnion
Notes: Christos: edited the slide

## Slide 2: HW is fast, but SW is a Bottleneck
64-byte TCP Echo:
Chart: 
| Microseconds
HW Limit | 10
Linux | 0
IX | 0
Chart: 
| Requests per Second
Line Rate | 8800000
Linux
IX
Notes: HW in black, Linux in Red, White for IX (or Tan)
Making it a build: 1.) Hardware is fast 2.) Software is a bottleneck

## Slide 3: HW is fast, but SW is a Bottleneck
64-byte TCP Echo:
Chart: 
| Microseconds
HW Limit | 10
Linux | 48
IX
Chart: 
| Requests per Second
Line Rate | 8800000
Linux | 1000000
IX
4.8x
Gap
8.8x
Gap
Notes: HW in black, Linux in Red, White for IX (or Tan)
Making it a build: 1.) Hardware is fast 2.) Software is a bottleneck

## Slide 4: IX Closes the SW Performance Gap
64-byte TCP Echo:
Chart: 
| Microseconds
HW Limit | 10
Linux | 48
IX | 11.4
Chart: 
| Requests per Second
Line Rate | 8800000
Linux | 1000000
IX | 8800000
Notes: HW in black, Linux in Red, White for IX (or Tan)
Making it a build: 1.) Hardware is fast 2.) Software is a bottleneck
Just say #2 on the slide

## Slide 5: Two Contributions
#1: Protection and direct HW access through virtualization
#2: Execution model for low latency and high throughput
Chart: 
| Microseconds
HW Limit | 10
Linux | 48
IX | 11.4
Chart: 
| Requests per Second
Line Rate | 8800000
Linux | 1000000
IX | 8800000
Notes: HW in black, Linux in Red, White for IX (or Tan)
Making it a build: 1.) Hardware is fast 2.) Software is a bottleneck
Just say #2 on the slide
Christos: edited the slide

## Slide 6: Why is SW Slow?
Created by: Arnout Vandecappelle
http://www.linuxfoundation.org/collaborate/workgroups/networking/kernel_flow
Complex Interface
Code Paths Convoluted by Interrupts and Scheduling
Notes: Show asynchronous behavior

## Slide 7: Problem: 1980s Software Architecture
Berkeley sockets, designed for CPU time sharing
Today’s large-scale datacenter workloads:
Hardware: Dense Multicore + 10 GbE (soon 40)
API scalability critical!
Gap between compute and RAM -> Cache behavior matters
Packet inter-arrival times of 50 ns
Scale out access patterns
Fan-in -> Large connection counts, high request rates
Fan-out -> Tail latency matters!
Notes: Large scale data center workloads
Memory access latencies have changed
Very general unifying abstraction
Tradeoffs back then were such that you could do this without hurting performance
Easy intuitive explanation of quantitative trends
Don’t emphasize berkenely sockets

## Slide 8: Conventional Wisdom
Bypass the kernel
  Move TCP to user-space (Onload, mTCP, Sandstorm)
  Move TCP to hardware (TOE)
Avoid the connection scalability bottleneck
  Use datagrams instead of connections (DIY congestion management)
  Use proxies at the expense of latency
Replace classic Ethernet
  Use a lossless fabric (Infiniband)
  Offload memory access (rDMA)
Common thread: Give up on systems software
Notes: Just say what we do, push this to discussion end of paper
Shown how IX does it, this turns out to be very different from how people have done it in the past
TOE might be in the wrong place

## Slide 9: Our Approach
Bypass the kernel
  Move TCP to user-space (Onload, mTCP, Sandstorm)
  Move TCP to hardware (TOE)
Avoid the connection scalability bottleneck
  Use datagrams instead of connections (DIY congestion management)
  Use proxies at the expense of latency
Replace classic Ethernet
  Use a lossless fabric (Infiniband)
  Offload memory access (rDMA)
Tackle the problem head on…
Robust Protection
Between App
and Netstack
Connection
Scalability
Commodity 10Gb
Ethernet

## Slide 10: Separation of Control and Data Plane
DP
DP
Host Kernel
CP
Userspace
Kernelspace
C
C
C
C
C
Notes: 1.) Well this is not new, we separate the controlplane from the dataplane and the host operating system is really just used to allocate resources in a course-grained manner
At this point the diagram is actually not very different from arrakis or userspace TCP
2.) Show queues
3.) click in extra protection layer
4.) Rather than building a hypervisor we use the dune kernel module
5.) Reveal dataplane internals and library

## Slide 11: Separation of Control and Data Plane
DP
DP
Host Kernel
CP
Userspace
Kernelspace
C
C
C
C
C
RX
TX
RX
TX
RX
TX
RX
TX
Notes: 1.) Well this is not new, we separate the controlplane from the dataplane and the host operating system is really just used to allocate resources in a course-grained manner
At this point the diagram is actually not very different from arrakis or userspace TCP
2.) Show queues
3.) click in extra protection layer
4.) Rather than building a hypervisor we use the dune kernel module
5.) Reveal dataplane internals and library

## Slide 12: Separation of Control and Data Plane
IX DP
IX DP
Host Kernel
IX CP
C
C
C
C
C
RX
TX
RX
TX
RX
TX
RX
TX
Ring 3
Guest
Ring 0
Host
Ring 0
Notes: 1.) Well this is not new, we separate the controlplane from the dataplane and the host operating system is really just used to allocate resources in a course-grained manner
At this point the diagram is actually not very different from arrakis or userspace TCP
2.) Show queues
3.) click in extra protection layer
4.) Rather than building a hypervisor we use the dune kernel module
5.) Reveal dataplane internals and library

## Slide 13: Separation of Control and Data Plane
IX DP
IX DP
Linux kernel
IX CP
C
C
C
C
C
RX
TX
RX
TX
RX
TX
RX
TX
Ring 3
Guest
Ring 0
Host
Ring 0
Dune
Notes: 1.) Well this is not new, we separate the controlplane from the dataplane and the host operating system is really just used to allocate resources in a course-grained manner
At this point the diagram is actually not very different from arrakis or userspace TCP
2.) Show queues
3.) click in extra protection layer
4.) Rather than building a hypervisor we use the dune kernel module
5.) Reveal dataplane internals and library

## Slide 14: Separation of Control and Data Plane
Linux kernel
IX CP
C
C
C
C
C
RX
TX
RX
TX
RX
TX
RX
TX
Ring 3
Guest
Ring 0
Host
Ring 0
Dune
IX
libIX
Memcached
IX
libIX
HTTPd
Notes: 1.) Well this is not new, we separate the controlplane from the dataplane and the host operating system is really just used to allocate resources in a course-grained manner
At this point the diagram is actually not very different from arrakis or userspace TCP
2.) Show queues
3.) click in extra protection layer
4.) Rather than building a hypervisor we use the dune kernel module
5.) Reveal dataplane internals and library

## Slide 15: The IX Execution Pipeline
event-driven app
libIX
RX
TX
TCP/IP
2
RX
FIFO
Event
Conditions
3
Batched
Syscalls
TCP/IP
Timer
4
5
6
Ring 3
Guest
Ring 0
1
Notes: Synchronous not asynchronous

## Slide 16: Design (1): Run to Completion
event-driven app
libIX
RX
TX
TCP/IP
2
RX
FIFO
Event
Conditions
3
Batched
Syscalls
TCP/IP
Timer
4
5
6
Ring 3
Guest
Ring 0
1
Improves Data-Cache Locality
Removes Scheduling Unpredictably
Notes: Design is for event-based application
Asychronous, non-blocking, batched system calls

## Slide 17: Design (2): Adaptive Batching
event-driven app
libIX
RX
TX
TCP/IP
2
RX
FIFO
Event
Conditions
3
Batched
Syscalls
TCP/IP
Timer
4
5
6
Ring 3
Guest
Ring 0
1
Improves Instruction-Cache Locality and Prefetching
Adaptive Batch
Calculation
Notes: Okay I fixed latency, now I need to fix throughput. But batching kills latency, how do I do this, by using “adaptive batching”
Animate a packet a second bubble, each phase animated
Show scratch pad between stages

## Slide 18: See the Paper for more Details
Design (3): Flow consistent hashing
  Synchronization & coherence free operation
Design (4): Native zero-copy API
  Flow control exposed to application
Libix: Libevent-like event-based programming
IX prototype implementation
  Dune, DPDK, LWIP, ~40K SLOC of kernel code
Notes: Christos: edited the slide

## Slide 19: Evaluation
Comparison IX to Linux and mTCP [NSDI ’14]
TCP microbenchmarks and Memcached
10GbE Switch
~ 25 Linux Hosts
IX
IX
1x10GbE
4x10GbE
w/ L3+L4 bond
Notes: Bonding 4x10gbe makes for a logical 40gbe NIC

## Slide 20: TCP Netpipe
½ Bandwidth
@ 20 KB
½ Bandwidth
@ 135 KB
5.7 us ½ RTT

## Slide 21: TCP Echo: Multicore Scalability for Short Connections
IX 10GbE
IX 4x10GbE
Linux 10GbE
Linux 4x10GbE
mTCP 10GbE
Saturates
1x10GbE
Notes: IX saturates at 3 cores
mTCP can saturate but it needs all the cores
Linux never gets anywhere close
Minimal message size for 50% of bandwidth

## Slide 22: Connection Scalability
~10,000 Connections
Limited by L3

## Slide 23: Memcached over TCP
IX (p99)
IX (avg)
Linux (p99)
Linux (avg)
3.6x More RPS
2x Less Tail Latency
6x Less Tail Latency
With IX clients
Notes: Using Linux clients, we’ve experimented with IX on the client
If we change the client we can get another 6x tail latency improvement

## Slide 24: IX Conclusion
A protected dataplane OS for datacenter applications with an event-driven model and demanding connection scalability requirements
Efficient access to HW, without sacrificing security, through virtualization
High throughput and low latency enabled by a dataplane execution model
Notes: Thank you for your attention and I’ll take any questions
Immediately have unanimated figures next

## Slide 25: Separation of Control and Data Plane
Linux kernel
IX CP
C
C
C
C
C
RX
TX
RX
TX
RX
TX
RX
TX
Ring 3
Guest
Ring 0
Host
Ring 0
Dune
IX
libIX
Memcached
IX
libIX
HTTPd
Notes: 1.) Well this is not new, we separate the controlplane from the dataplane and the host operating system is really just used to allocate resources in a course-grained manner
At this point the diagram is actually not very different from arrakis or userspace TCP
2.) Show queues
3.) click in extra protection layer
4.) Rather than building a hypervisor we use the dune kernel module
5.) Reveal dataplane internals and library

## Slide 26: The IX Execution Pipeline
event-driven app
libIX
RX
TX
TCP/IP
2
RX
FIFO
Event
Conditions
3
Batched
Syscalls
TCP/IP
Timer
4
5
6
Ring 3
Guest
Ring 0
1
Notes: Synchronous not asynchronous

## Slide 27: Adaptive Batching w/ Memcached

## Slide 28: Connection Scalability Counters

## Slide 29: Another Memcached Workload

## Slide 30: TCP Echo: Long Connections
IX 10GbE
IX 4x10GbE
Linux 10GbE
Linux 4x10GbE
mTCP 10GbE
Notes: IX is the black line

## Slide 31: TCP Echo: Message Size
IX 10GbE
IX 4x10GbE
Linux 10GbE
Linux 4x10GbE
mTCP 10GbE

## Slide 32: TCP Echo
Baseline parameters:
8 cores (1 socket)
1 echo per connection
64 byte message size
Connection Duration
Multicore Scalability
Message Size
IX 10GbE
IX 4x10GbE
Linux 10GbE
Linux 4x10GbE
mTCP 10GbE