## Slide 1
IX: A Dataplane Operating System for
High Throughput and Low Latency
Adam Belay1, George Prekas2, Ana Klimovic1, Samuel Grossman1, Christos Kozyrakis1, Edouard Bugnion2
Introduction
Datacenter applications such as search and social networking are redefining the requirements for systems software networking stacks:
Microsecond tail latency
High packet rates for short messages
Connection scalability
Protection
Resource efficiency
Current Approaches
Bypass the kernel
  User-level stack (e.g. Openonload, mTCP)
  Offload networking to HW (e.g. RDMA, TOE)
  Replace TCP (e.g. UDP, Infiniband)
Sacrifice security
  Bandwidth metering, ACLs, flow control, firewalling, and protocol correctness
  Policy enforcement limited by HW
IX System Architecture
Network Processing in IX
Introducing IX
IX reconciles security and performance
  Implements full TCP stack in dataplane, protected from application
  Saturates 10 GbE NICs with 64b msgs
  Achieves up to 3.6x more RPS and 2x less tail latency compared to Linux for Memcached workloads
Separation of Control and Data
Linux is the control plane
  Course grained resource management (e.g. large pages, network queues)
  Performs management functions and load balancing
IX is the data plane (powered by Dune)
  Inspired by network middleboxes
  A custom single-app OS for high performance networking
Three-way isolation between App, DP, CP
Results Summary
Outperforms Linux and mTCP by 10× and 1.9×, respectively, for throughput
Achieves unloaded uni-directional latency of 5.7µs, 4× better than Linux and an order of magnitude better than mTCP
Improves memcached throughput by up to 3.6× with 2× less tail latency than Linux
Scales to 105-order connections
Reduces percentage of kernel time from ~75% (for Linux) to < 10% (for IX)
Connection Duration
Multicore Scalability
Message Size
Key:
IX 10GbE
IX 4x10GbE
Linux 10GbE
Linux 4x10GbE
mTCP 10GbE
Memcached
Adaptive Batching
TCP Echo
Contact Email:
abelay@stanford.edu
1
2
IX Design Principles
Run to completion
  Improves D-cache behavior
Adaptive batching
  Every step (1 – 6) is batched, but only during congestion
  Improves I-cache behavior
Native zero copy API
  Maximizes programming model flexibility
Flow consistent hashing + coherence free
  Improves multicore scalability
Motivation
10 GbE networking hardware is incredibly fast
  Over 10 million QPS possible w/ small pkts
  10 – 20 μs latency possible inside datacenters with cut-through switching
  Only getting better: 40 GbE around the corner
Systems software is a significant bottleneck
  Limited throughput, latency jitter, poor multicore scalability